## Slide 1: PS3 DSIVE TEAM
Final Presentation: Cell Broadband Engine (CBE) Real World Application
12/10/2007
Sponsored by:

## Slide 2: Group Members
Syed Ali
Mechanical/Electrical Engr
Paul Ireifej
Comp Systems Engr / Computer Science
Justin Law
Comp Systems Engr
Carlos Lazo
Comp Systems Engr
Tarzi Mahmutcan
Comp Systems Engr / Computer Science
Nick Matthews
Comp Systems Engr / Computer Science
Shahab Rastegar
Electrical Engr
Thomas Smith
Comp Systems Engr
Notes: Carlos

## Slide 3: Outline
Sponsors
Objectives
System Design & Demonstrations
Accomplishments
Open Issues & Recommendations
Conclusions

## Slide 4: Problem

## Slide 5: IBM
Explore viability of O/S installation on the PS3
Research usability/capabilities of the CBE
Develop a new application that harnesses the computational power of the CBE
Utilize IBM’s development tools (IBM CBE SDK)
Realistically assess the CBE learning curve over a 3 month period

## Slide 6: GE
Develop a non-invasive system to measure the rate of metallic erosion on steam turbines
Implement a modular unit that can interface with the turbines using existing mechanical portals
Automate the task of measuring, quantifying and reporting erosion levels

## Slide 7: Current Industrial Solution
Manually Open
Disadvantages
$500,000 per Service
Complicated Process
Unknown Rate of Erosion

## Slide 8: Proposed System Architecture

## Slide 9: Semester Objectives
Install O/S
Install IBM SDK for development
Establish network connectivity & access
Create image capture hardware for simulation
Communicate with PS3 via FTP
Analyze image in PGM format
Utilize the parallel computing power of the CBEA
Implement parallel processing via multi-threading
Optimize software code for multiple processors
Optimize PGM images for image processing
Develop image processing and analysis algorithm
Create output log

## Slide 10: Design Methodology & Strategy
Model & prototype ideas in MATLAB
Code translated into C from MATLAB
Successfully port and run functions on PS3 using Cell SDK Environment
Vectorize code
Concurrently build simulation hardware for future independent image testing

## Slide 11: Imaging Concepts Considered
Subtraction
  Consistent lighting
  Requires prefect alignment
Average Distance
  Sufficient lighting on the edge of the blade, and on the scribed line.
Edge Size Standard Deviation
  The total number of steps needed to implement this method is greater than the other two methods.
  Matrox based Level Setting Edge Detection
Level Setting Edge Detection
  Complex mathematics
  Difficult to implement outside of MatLab
High Pass Filter Edge Detection
  Least process intensive
  Easily implemented
  Sufficient accuracy

## Slide 12: Demonstration Level Setting
Contour Technique
  Tracks changes in shapes
  Types of shapes: splits, hole development and geometric deviations
Time variant function
  Based on number of iterations for accuracy

## Slide 13: Demonstration MatLab Edge Detection

## Slide 14: Demonstration MatLab Edge Detection
Average Displacement: 17 Standard Deviation: 4.196
Average Displacement: 2 Standard Deviation: 0.651
Average Displacement: 15 Standard Deviation: 3.419
Average Displacement: 51 Standard Deviation: 14.204
Average Displacement: 15 Standard Deviation: 1.910
Average Displacement: 86 Standard Deviation: 12.422

## Slide 15: System Design PPU / SPU Information Exchange
One Power Processing Element (PPE) that controls eight Synergistic Processing Elements (SPE)
Team is using SDK 2.1 and “libspe2.h”
Each SPE includes a Memory Flow Control (MFC) that includes direct memory access

## Slide 16: Demonstration PPU / SPU Information Exchange
Size of Square Matrix | Convolution on ThinkPad T61 | Convolution on PPE | Estimated with PPU/SPU parallel processing (4 SPE’s)
10 | < 10 ms | < 10 ms | < 10 ms
100 | 10 ms | 10 ms | 2.5 ms
255 | 28 ms | 60 ms | 15 ms
500 | 98 ms | 230 ms | 57.5 ms
1000 | 485 ms | 940 ms | 235 ms
2048 | 1,705 ms | 3,930 ms | 982.5 ms
5096 | 10,181 ms | 26, 570 ms | 6,642.5 ms

## Slide 17
System Design
FTP Connection from Image capture hardware
PS3 Hard drive
Convert Image format to PGM
Create Matrix with int_matrix function
Blur image with blur kernel
Segment image colors
Implement edge detection
Calculate Standard Deviation
Output

## Slide 18: System Design
BEFORE
AFTER
End to End System
  Shell script developed for linking code together
  Manual runs performed on test images
  Accuracy of timer in hundredths of a second
  Estimated times:
    Intel Processor on T61: 1-2 seconds
    PS3 PPU: 60 ms (approximately 10 ms/operation)

## Slide 19: System Design Simulation Hardware
Testing Apparatus for End-to-End System
Serves as a Simplified Image Capturing System for PS3 Erosion Image Analysis
Consists of a Turbine Simulator and an Image Capturing System
Projects can be Easily Integrated Together

## Slide 20: Demonstration Simulation Hardware

## Slide 21: Accomplishments
Linux O/S installation and connectivity
Image processing analysis and implementation
Code development and migration to PS3
Successful parallel communication with four PS3 sub-processors
End-to-end system with time estimates
Mechanical construction of simulation hardware

## Slide 22: Open Issues & Recommendations Image Processing
Require static variables
Unresolved code issues
Accuracy of edge detection
FTP script not implemented

## Slide 23: Open Issues & Recommendations PPU / SPU Information Exchange
Unable to send an array parameter to an SPE
Function “mfc_get” initiates a transfer into the local store and function “mfc_put” initiates a transfer back into main memory
When including “spu_mfcio.h”, “spu_internals.h” returns error with “vec_float4” type
Recommendation: Begin development with SDK 3.0

## Slide 24: Recommendations Simulation Hardware
More Complex LabView Program/Control
Faster Camera (1/1000 Minimum Shutter)
Use NI USB 6009 DAQ Card (Less Lag Time)
Use White LEDs & Better Turbine Blade Model
Configure FTP Connection for PS3
Use Windows XP for LabView (DAQ Drivers)

## Slide 25: Conclusions
Image processing algorithms heavily dependant on quality & content of image
IBM SDK suitable for project
Automated image analysis would be worthwhile for GE
Cell broadband processor surpasses processing power needed for current image algorithms

## Slide 26: Lessons Learned
PS3 Cell Architecture and Linux O/S learning curve is steep given the time period
One will face unexpected problems with the PS3 cell processor (uncharted territory)
Sub team communication integral to the speed and success of the project
Worthwhile to provide an entry level module to the Cell Processor

## Slide 27
*** THANK YOU FOR THIS OPPORTUNITY ***
QUESTIONS ?