## Slide 1: Robotics II Final Project
2D Terrain Traversal
Ben Consolati
Carlos Lazo

## Slide 2: Goals
Get the car across the terrain efficiently
Please fix this Carlos :P

## Slide 3: Implementation – The Vehicle
The vehicle is a 2D body with two circles attached as wheels
The vehicle moves by applying torque to these wheels
At any given point in time, the car either applies Forward torque or Backward torque
The direction of torque is governed by “Control Plans”

## Slide 4: Implementation – Control Plan
The “Control Plan” is an array of ones and zeros, called “Control Steps”
Ones represent “Forward Torque”
Zeros represent “Reverse Torque”
Each index in the array represents a time interval
As time passes, the vehicle progresses through the Control Steps, applying the appropriate torque

## Slide 5: Control Plan Example
Assume the time interval for each Control Step is one second
Given the Control Plan: [ 1 0 1 1 0 ]
The torque on the car's wheels would be:
  Forward during the 1st second
  Reverse during the 2nd second
  Forward during the 3rd second
  Forward during the 4th second
  Reverse during the 5th second

## Slide 6: Implementation – Runs
The simulation is made up of “Runs” that are carried out one after another
Each Run implements a new Control Plan
In general, each Control Plan is generated with reverse binary counting, starting with “All Forwards”
By iterating through every Control Plan, we can find the optimal Control Plan

## Slide 7: Runs Example
The first run’s Control Plan is always “All Forward” or [ 1 1 1 1 … 1 ]
For a simulation with Runs consisting of five Control Steps, the first few runs would be:
  [ 1 1 1 1 1 ]
  [ 1 1 1 1 0 ]
  [ 1 1 1 0 1 ]
  [ 1 1 1 0 0 ]

## Slide 8: Implementation - Optimization
When a car gets stuck or falls off platform, we can stop the current Run at this “Failure Step” and start the next run
Much more significantly, we know that further modifications to the Control Plan after the Failure Step will have no affect on the outcome of the simulation

## Slide 9: Optimization Example
We start with the Control Plan: [ 1 1 1 1 1 ]
During the Run, the vehicle gets stuck during the third Control Step
Next scheduled Control Plan is: [ 1 1 1 1 0 ]
But we know the vehicle will just get stuck on the third step again, modifying steps after Failure Step will do nothing
Next Control Plan should be [ 1 1 0 1 1 ] since this has a chance to prevent the Failure Step

## Slide 10: Implementation – The Modes
Three different simulation modes
Stop On First Success:
  Simulation stops as soon as a Run gets the vehicle across the terrain.
Exhaustive:
  Carries out every unique Run and records results (still incorporates optimization).
Find Fastest:
  Same as exhaustive except that it stops Runs short if they run longer than a solution found in a previous Run. More efficient if you’re just looking for the optimal solution.

## Slide 11: Challenges
Stuck Recognition
  What we perceive as “stuck” is often “very slightly moving” in DVC
  We don’t want to falsely detect being stuck when vehicle can still move